## Slide 1: What wearable IMUs reveal about obstacle crossing
Machine-learning and biomechanics results
10 young adults · Tests 101–110
Ehsan Sharafian · 30 October 2026
Notes: Results of the machine-learning and biomechanics analyses of the obstacle-crossing study (Tests 101-110). All analyses run in MATLAB; reports and figures are in Results/ML Models/MATLAB. Every accuracy is for a participant the model never saw.

## Slide 2: The answer in brief
Obstacle height can be read from two foot IMUs; obstacle width cannot.
92 %
obstacle height (3 levels) recognised on a new person once scaled to their crossings
+10 mm
extra foot lift per cm of obstacle; the safety margin stays constant
0.7 s
lead time: height is ~80 % known at the lead-foot apex, before the trailing foot lifts
86 %
end to end without a camera: crossing found, legs paired, height correct
Limits: obstacle width (5 vs 15 cm) is barely recognisable (best 65 %, chance 50 %) because people cross both widths alike, and the toe-clearance margin cannot be estimated.
Notes: Four headline findings and one limit. 92 % = two foot IMUs, person scaling, lead and trail models combined (95 % CI 87-96). 0.7 s = median time from the lead-foot apex to the trailing toe-off (683 ms). 86 % = camera-free pipeline (detect, pair, classify); 83.5 % if missed crossings are counted as errors.

## Slide 3: Study design and evaluation
Every accuracy in this deck is for a participant the model never saw in training.
10 young adults
260 obstacle crossings used for ML (303 recorded), about 5 per obstacle
6 Movella Dot IMUs
thigh, shank and foot of both legs; camera motion capture as the reference
6 obstacles
3 heights (10 / 20 / 30 % of leg length) × 2 widths (5 / 15 cm)
width 5 cm
10 %
20 %
30 %
width 15 cm
10 %
20 %
30 %
How the models were tested
Leave-one-participant-out: train on 9 people, test on the 10th, for all 10
Balanced accuracy; chance 33 % (height), 50 % (width), 17 % (6 obstacles)
95 % CI by participant bootstrap; permutation tests shuffle labels within each person
Leading and trailing legs modelled separately, then combined by soft vote
Person scaling: each feature scaled by the person's own crossings (median / IQR, no labels)
Notes: 260 obstacle crossings had complete IMU and camera data (include_ml); 303 were recorded. Generic model = features scaled only to the person's level walk and leg length. Person scaling = each feature scaled by the person's own median and IQR over their crossings; it uses no height labels. Crossing order was never used as a feature.

## Slide 4: How people cross an obstacle
How the crossing scales with obstacle height, where the information sits, and what makes each person different
01
Notes: Section 1: the biomechanics. These results explain why the models behave as they do.

## Slide 5: Foot lift scales 1:1 with obstacle height
People raise each foot by about the obstacle height and keep their safety margin constant.
One line per participant; slopes from a mixed model (random intercept and slope per person).
Mechanism: lead thigh flexion +1.2° per cm; trailing heel-up (shank tilt −1.2° per cm).
+10.1 mm
lead foot lift per cm of obstacle (95 % CI 9.4–10.8)
+11.1 mm
trailing foot lift per cm (CI 9.7–12.6)
−0.7 mm
change in the lead safety margin per cm: not significant (CI −1.8 to +0.4); trailing −2.3 mm, n.s.
Notes: Mixed-effects model, random intercept and slope per participant, 260 crossings. Lead foot lift +10.08 mm per cm (9.38-10.78); trailing +11.12 mm per cm (9.66-12.59). Camera safety margin: lead -0.71 mm per cm (p = 0.185), trailing -2.32 mm per cm (p = 0.055): neither significant. Lead thigh +1.19 deg per cm; trailing shank -1.19 deg per cm (heel-up).

## Slide 6: Height is encoded mid-swing; width is not
Share of within-person variance explained by the obstacle (eta²) at each moment of the swing.
Width: eta² ≤ 0.08 in every signal at every moment (right panels); the crossing barely changes with width.
0.62
lead foot height around the apex (48 %)
0.45
lead thigh tilt (62 % of swing)
0.76
trailing foot height, early swing (20 %)
0.66
trailing shank tilt at push-off (4 %)
Notes: eta squared = share of the within-person variance explained by obstacle height (left panels) or width (right panels), at each 2 % of the swing (toe-off to heel-strike). Peaks: trailing foot height 0.76 at 20 %, trailing shank tilt 0.66 at 4 %, lead foot height 0.62 at 48 %, lead thigh tilt 0.45 at 62 %. Width stays at or below 0.08 everywhere.

## Slide 7: Every walker has a strong signature
Raw crossings cluster by person; only after person scaling do they order by obstacle height.
99.2 %
of crossings matched to the right person from one crossing (chance 10 %)
99 of 110
features vary more between people than between obstacle heights
0.48
cluster strength by person (silhouette); by height only 0.26, after person scaling
What it means
A generic model sees the person first and the obstacle second, so it stalls at 62–73 %. Scaling each feature to the person removes the signature and lifts accuracy to ~90 %.
Notes: A logistic model identifies the participant from the features of one crossing with 99.2 % balanced accuracy (5-fold; chance 10 %). In 99 of the 110 features the person explains more variance than the obstacle height. t-SNE of the 110 features: silhouette by participant 0.48 and by height -0.04 for the raw features; by height 0.26 after person scaling.

## Slide 8: The personal margin caps generic models
Each person's extra lift for any obstacle varies by two-thirds of the step between heights.
Chart: Foot lift, mm
| Lead foot lift | Trailing foot lift
Spread across people (SD of personal margin) | 64 | 76
Step between two neighbouring heights | 98 | 105
Hard to predict in advance
r = 0.43 with the person's normal walking and 0.20 with leg length (lead foot)
Why generic models stall
an unseen person's offset pushes crossings toward a neighbouring height: 62–73 %
What fixes it
a few of the person's own crossings, labelled or not, reveal the offset: ~90 %
Notes: Personal margin = the lift predicted by each participant's own dose-response line at the cohort's mean obstacle height. Between-person SD 64 mm (lead) and 76 mm (trailing) against steps of 98 and 105 mm between neighbouring heights (ratios 0.66 and 0.72). Correlation with the level-walk value: 0.43 lead, -0.22 trailing; with leg length 0.20 and 0.04.

## Slide 9: Lead leg, coupling and first encounters
Crossing strategy is not fixed by dominance, and each leg adapts on its own.
45 %
of crossings were led with the dominant leg; most people alternate
A device needs a sensor on each foot (the IMU tells lead from trail 100 %).
r ≈ 0.1
between the two legs' lift deviations within a crossing
The trailing foot does not correct the lead foot: each leg carries its own information.
+12 mm
extra lead-foot lift on the first crossing of a new obstacle (CI +5 to +20)
People are more cautious at a first encounter, then settle.
Notes: 45 % of the 303 crossings were led with the dominant leg (lab sheet); the IMU recovers the leading leg in 100 % of crossings. Coupling: correlations of the crossing-to-crossing deviations from each participant x obstacle mean are r = 0.11, -0.12, -0.05 and -0.07 for the pairs tested. First crossing of a new obstacle: +11.7 mm lead lift (CI 4.7-19.9) above the participant x obstacle mean.

## Slide 10: Recognising obstacle height
Accuracy on a person the model has never seen: generic vs person-scaled models, sensors, timing and precision
02
Notes: Section 2: recognising obstacle height. Three levels, chance 33 %.

## Slide 11: Height accuracy rises from 62 % to 92 %
Obstacle height (3 levels, chance 33 %) on an unseen participant; balanced accuracy.
Chart: Balanced accuracy, unseen participant
| Generic · 57 summary features | Generic · fair nested selection | Generic · 13 clearance-shape features | Person-scaled · deep learning (1D CNN) | Person-scaled · all 6 IMUs | Person-scaled · fair nested selection | Person-scaled · two foot IMUs
Balanced accuracy | 0.621 | 0.694 | 0.728 | 0.877 | 0.912 | 0.915 | 0.923
Generic (grey)
ceiling of 62–73 %: the person's offset shifts every crossing
Person-scaled (orange)
about +20 points, with no labels. Fair nested choice: 91.5 % (CI 86–97); weakest person 73 %.
Notes: All results leave-one-participant-out. Generic: 57 summary features of the leading leg, logistic regression, 62.1 %. Clearance-shape features: 13 features of how long and how far the lead foot stays high, apex position and foot tilt at the apex (72.8 %, p = 0.003). Fair nested selection = the setting is chosen inside the training folds only: generic settings 69.4 % (CI 58-80); all 36 settings 91.5 % (CI 86-97). Two foot IMUs with person scaling 92.3 % (CI 87-96). Permutation tests p <= 0.003.

## Slide 12: The foot carries both legs' information
Height accuracy from one signal at a time (person scaling, random forest).
Chart: Balanced accuracy from a single signal
| Thigh tilt | Shank tilt | Foot tilt | Foot path | Foot accel.
Leading leg | 0.774 | 0.498 | 0.881 | 0.849 | 0.369
Trailing leg | 0.442 | 0.782 | 0.834 | 0.845 | 0.54
Leading leg
the thigh lifts the foot over: thigh tilt alone 77 %
Trailing leg
push-off with heel-up: shank tilt alone 78 %
Foot IMU
tilt and path carry both legs (83–88 %); acceleration alone is weak
Notes: Each bar is a random forest on one signal only, person scaling, leading or trailing leg. Foot tilt 88.1 / 83.4 %, foot trajectory (ZHC) 84.9 / 84.5 %, thigh tilt 77.4 / 44.2 %, shank tilt 49.8 / 78.2 %, foot acceleration 36.9 / 54.0 % (lead / trail).

## Slide 13: Height is known 0.7 s before trail toe-off
Accuracy from the leading leg's data up to each moment of its swing (forest; chance 33 %).
Chart: Balanced accuracy, unseen participant
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Person scaling | 0.521 | 0.653 | 0.677 | 0.742 | 0.797 | 0.778 | 0.797 | 0.885 | 0.876 | 0.864 | 0.858
Generic (level-walk scaling) | 0.401 | 0.465 | 0.524 | 0.54 | 0.593 | 0.635 | 0.624 | 0.647 | 0.612 | 0.567 | 0.566
Lead toe-off
983 ms before trail toe-off · 52 %
Lead foot apex
683 ms before · about 80 %
Lead landing
417 ms before · 86 %
Trailing toe-off
the cue must arrive by now
Notes: Lead-leg data up to x % of its swing, random forest. With person scaling: 52.1 % at lead toe-off, about 78-80 % by the lead-foot apex (median 54 % of the swing, 683 ms before the trailing toe-off), 88.5 % at 70 %, 85.8 % at lead landing (417 ms before). The generic model stays at 40-65 %. Median times over 260 crossings.

## Slide 14: Height in centimetres and from raw curves
Two further checks: predict height as a number, and learn straight from the swing curves.
Height as a number (regression)
2.4 cm
mean absolute error
0.91
correlation r
85 %
nearest height right
Neighbouring heights differ by 8.3–10.6 cm (10 % of leg length): the typical error is about a quarter of a step.
Two foot IMUs, lead + trail vote, person scaling, random forest.
Deep learning on raw curves
88 %
height, person-scaled
56 %
width (chance 50 %)
54 %
height, generic
No hand-made features: the information is in the curves. At n = 10 the compact clearance features stay ahead (92 %).
1D convolutional network on the six swing curves of each leg (51 samples each).
Notes: Regression: lead + trail vote, person scaling, random forest: mean absolute error 2.37 cm, r = 0.91; rounding to the nearest height gives 85.2 %. CNN: two convolution layers on the six raw swing curves of each leg (51 samples each). Person scaling: 79.9 % lead, 83.1 % trail, 87.7 % combined; width 56.0 %. Generic (level) scaling: 54.4 % for height.

## Slide 15: Obstacle width is barely recognisable
Width (5 vs 15 cm, chance 50 %) stays near chance with every sensor and model.
Chart: Width, balanced accuracy (chance 50 %)
| IMU · generic model (best) | IMU · person scaling (best) | IMU · within each height | IMU · sideways motion only | Camera · foot placement
Balanced accuracy | 0.61 | 0.646 | 0.605 | 0.538 | 0.576
All 6 obstacles at once
chance 17 %
29 %
generic
61 %
person-scaled
Of these, the height part is right 91 % of the time and the width part 63 %: height is recognised, width adds little beyond guessing.
Notes: Width (chance 50 %): generic forest, leading leg 61.0 %; person scaling, leading leg, logistic 64.6 % (p = 0.003); within each height 60.5 %; out-of-plane features only 53.8 %; camera foot placement 57.6 %. Six obstacles (chance 17 %): generic logistic 29.1 %; person scaling, forest, lead + trail 61.2 %.

## Slide 16: People cross both widths the same way
The limit is behavioural, not the sensor: a 10 cm wider obstacle barely changes the crossing.
+4 cm
longer crossing step for a 10 cm wider obstacle (camera; 8 of 10 people)
≤ 0.08
share of within-person variance due to width in any swing curve (height: up to 0.76)
≤ 0.06
the same for sideways tilt, twist and the outward foot path
57.6 %
width from the camera's own foot placement (chance 50 %)
What it means
A wearable can tell how high to lift the foot, not how far to step. Width cues would need a sensor that sees the obstacle itself.
Largest share of within-person variance
height
0.76
width
≤ 0.08
Notes: Camera foot placement relative to the obstacle centre: crossing step (trail toe to lead heel) +37 mm for the 15 cm obstacle, positive in 8 of 10 participants, eta squared 0.02. Width eta squared stays at or below 0.08 in all six swing curves of both legs. Out-of-plane features (sideways tilt and heading of thigh, shank and foot; outward foot path): largest width effect 6 % of the variance; width from these alone 53.4-53.8 %.

## Slide 17: Toward a wearable cueing device
Which sensors, how much calibration, real sessions, no camera, and real-time cues
03
Notes: Section 3: what a wearable obstacle-cueing device could do with these signals.

## Slide 18: Two foot IMUs are enough
Height accuracy by sensor set (person scaling; lead and trail models combined).
Chart: Balanced accuracy by sensor set
| 2 thigh | 2 shank | 2 foot | All 6 | 1 foot, right | 1 foot, left
Balanced accuracy | 0.804 | 0.794 | 0.923 | 0.912 | 0.829 | 0.909
Best site: the foot
tilt and path of both legs: 92.3 % (CI 87–96)
More sensors don't help
all six IMUs: 91.2 %
One foot only: 83–91 %
it leads in some crossings and trails in others
Notes: Person scaling, random forest, lead and trail models combined by soft vote. Thigh pair 80.4 %, shank pair 79.4 %, foot pair 92.3 % (CI 87-96), all six 91.2 % (CI 86-96). One foot IMU: right leg 82.9 %, left leg 90.9 %. The thigh carries the leading-leg information (77 %) and the shank the trailing-leg information (78 %).

## Slide 19: A little calibration goes a long way
Two foot IMUs on a new user: accuracy by what the device knows about that person.
Chart: Balanced accuracy on the new user
| Nothing · generic model | Nothing · clearance-shape features | 5 unlabelled crossings | 10 unlabelled crossings | 15 unlabelled crossings | All crossings of a session, unlabelled | 1 labelled crossing (any height) | 1 labelled crossing per height
Balanced accuracy | 0.564 | 0.728 | 0.714 | 0.812 | 0.851 | 0.923 | 0.803 | 0.878
No calibration
generic model only
Unlabelled
the device just watches the user cross (random crossings)
Labelled
the user confirms the height once (physics-informed offset model)
In the blocked study order, the first 15 crossings give only 67.9 %: they cover 1–2 obstacles.
Notes: Unlabelled = person scaling from n random crossings of the session, tested on the remaining ones. Labelled = physics-informed offset model: a within-person height score (ridge) plus one personal offset estimated from the labelled crossing(s). Alternatives: weighted logistic with one labelled crossing per height 74.6 %; offset from unlabelled crossings by a mixture model 77.0 %. First 5 / 10 / 15 crossings in the blocked order: 60.4 / 66.5 / 67.9 %.

## Slide 20: In mixed order the device learns quickly
Sessions shuffled 30×: the device starts generic, then scales to the crossings it has seen.
Chart: Balanced accuracy, by crossings walked
| 1–5 | 6–10 | 11–15 | 16–20 | 21+
Mixed obstacle order (realistic) | 0.719 | 0.751 | 0.829 | 0.879 | 0.913
Blocked study order | 0.7 | 0.46 | 0.56 | 0.812 | 0.903
79 %
mixed order, crossings 6–15 (blocked order: 51 %)
90 %
mixed order, from crossing 16 on (blocked: 89 %)
A blocked early history covers 1–2 obstacles and biases the scaling, so the study's blocked-order numbers are pessimistic for real use.
Notes: Each participant's crossings were shuffled 30 times. The device uses the generic model for the first 5 crossings, then person scaling from the crossings walked so far (no labels). Mixed: 71.9, 75.1, 82.9, 87.9, 91.3 % (82.2 % overall). Blocked: 70.0, 46.0, 56.0, 81.2, 90.3 % (69.6 % overall).

## Slide 21: No camera needed: 86 % end to end
From 7,250 raw strides: find the crossings, pair lead and trail strides, classify the height.
1 · Detect
98.7 %
of crossing strides found; 97.2 % of detections are real
2 · Pair
95.2 %
of crossings with the right lead and trail strides (first foot = lead)
3 · Classify
90.7 %
of found crossings get the right height
End to end
86.3 %
fully correct; 83.5 % of every crossing walked
Scaling must come from crossings: scaling to the person's normal walking instead gives only 52.9 % end to end. About 1.4 false crossings per person per session.
Notes: All 7,250 ZVP-to-ZVP strides of both feet; 595 are crossing strides. Detection: random forest on stride features scaled to the person's walking: 98.7 % recall, 97.2 % precision. Pairing: the first foot is the lead. Height: lead and trail forests, soft vote, features scaled to the person's detected crossings. Denominator: 293 crossings with a valid toe-off event (of 303).

## Slide 22: Real-time cue: about 3 in 4 correct
Only the leading leg's data exist when the cue is sent (mixed order, learning as it goes).
Chart: Share of crossings
| Apex · always cue | Apex · cue if p ≥ 0.6 | Landing · always cue | Landing · cue if p ≥ 0.6
Correct cue | 0.702 | 0.553 | 0.756 | 0.616
Wrong cue | 0.286 | 0.146 | 0.233 | 0.135
No cue | 0.012 | 0.301 | 0.012 | 0.249
Time left before the trailing foot lifts: 683 ms at the lead-foot apex, 417 ms at lead landing.
99 %
of leading-leg crossings detected at the foot apex, online
3
false detections per session (~725 strides)
79–82 %
of cues are right when the device cues only if confident (p ≥ 0.6)
Notes: Online features up to the lead-foot apex (683 ms before the trailing toe-off) or lead landing (417 ms). Mixed order, person scaling learned causally from earlier crossings. Correct cues after 15 crossings: 75.3 % at the apex, 83.5 % at landing. With p >= 0.6, 79.1 % and 82.0 % of the given cues are right, but 30 % and 25 % of crossings get no cue. Labels below 2 % are hidden (the 1.2 % no-cue shares).

## Slide 23: Confidence helps; more people barely do
Answering only when confident buys accuracy; the learning curve is flat from 2–3 people.
Chart: Answer only when confident
| all | ≥ 0.5 | ≥ 0.6 | ≥ 0.7 | ≥ 0.8
Crossings answered | 1 | 0.94 | 0.79 | 0.67 | 0.46
Accuracy on them | 0.923 | 0.939 | 0.966 | 0.977 | 0.983
Chart: More training participants
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Accuracy | 0.885 | 0.891 | 0.903 | 0.904 | 0.904 | 0.914 | 0.914 | 0.923
Notes: Two foot IMUs, person scaling, random forest. Left: answer only when the top class probability reaches the threshold; coverage 100, 94, 79, 67, 46 % with accuracy 92.3, 93.9, 96.6, 97.7, 98.3 %. Right: each unseen participant predicted by models trained on n random other participants (10 draws per n): 88.5 % with 2 people to 92.3 % with 9. The remaining errors come from person-to-person differences, which calibration addresses.

## Slide 24: Errors follow trailing-foot consistency
Per participant: person-scaled accuracy vs how consistently they lift the trailing foot (d′).
Chart: Accuracy with person scaling vs trailing-foot consistency
| 2.1 | 2.7 | 3.6 | 3.2 | 2.2 | 3.4 | 2.5 | 0.9 | 4.5 | 3.4
Participant | 0.94 | 0.9 | 1 | 0.96 | 0.96 | 0.97 | 0.85 | 0.73 | 0.96 | 0.96
r = 0.77
accuracy vs trailing d′ over the 10 participants (lead d′: r = 0.25)
73 %
participant 108, with the least consistent trailing lift (d′ 0.9 vs 2.1–4.5)
r = −0.66
for the generic model: its errors come from the personal offset instead
Notes: d' = separation of the three heights in units of the within-height SD, per participant. Lead d' relates weakly to person-scaled accuracy (r = 0.25). The generic model behaves differently: its accuracy falls with trailing consistency (r = -0.66), because its errors come from how far a person's personal margin is from the group. n = 10, so these correlations are indicative.

## Slide 25: What the IMUs could not do
Negative results, reported as findings.
Obstacle width
best 65 % (chance 50 %): people cross both widths alike
Toe-clearance margin
not estimable from the IMUs (r ≈ 0.04; within a person 0.28)
Near-contact detection
weak: AUC 0.63–0.73 for low-clearance crossings
Self-training
letting the model label the new user's crossings made it worse: 54–67 %
Previous normal stride
as a personal reference gives only ~60 %: the margin is not visible in ordinary walking
Offset from unlabelled crossings
a mixture model reaches 77 %, below simple person scaling (92 %)
Notes: Toe clearance: regression of the trailing clearance has a mean absolute error of 85 mm against 84 mm for predicting the mean; r = 0.04; within-person r median 0.28. Near-contact detection: AUC 0.63-0.73 depending on the clearance threshold (0.73 for clearance <= 0 mm, 15 events). Lead features do not predict trailing clearance (r = -0.14). Self-training on the new person: 54.0-67.1 %.

## Slide 26: How far to trust these numbers
The checks are strict, but n = 10 young adults: these are feasibility results.
Checks passed
Leave-one-participant-out everywhere; participant-bootstrap 95 % CIs
Permutation tests (labels shuffled within each person): p ≤ 0.003
Fair nested selection of settings: 91.5 % (CI 86–97)
MATLAB and Python agree: mean difference 0.0 (logistic) and 0.9 points (forest)
Crossing order was never used as a feature
Caveats
n = 10 young adults: confirm on new participants and on older adults
Clearance-shape features were designed after the first results: small optimism possible
Person scaling assumes the user's crossings cover several heights
Obstacles ran in blocks; mixed order was simulated by shuffling
Notes: MATLAB and Python implementations of the same models: logistic mean absolute difference 0.0 points (max 0.4), forest 0.9 (max 2.2). Permutation tests shuffle the labels within each participant. The clearance-shape features came from a few biomechanically guided iterations after the first results.

## Slide 27: Conclusions and next steps
1
Foot lift scales 1:1 with obstacle height; the safety margin is constant but personal.
2
Two foot IMUs recognise obstacle height on a new person at ~92 % once scaled to their crossings; 80 % with one labelled crossing.
3
A camera-free, real-time pipeline is feasible: 86 % end to end, and about 3 in 4 cues correct 0.4–0.7 s ahead.
Next steps
Record more participants, including older adults
Run the obstacles in mixed order to test learning during use live
Estimate toe height (sensor-to-toe geometry) for clearance
Prototype the haptic cue and test it online
Notes: Take-home messages and next steps. Width cannot be cued from body-worn IMUs; a cueing device would focus on obstacle height.